Trace files

---
The look
The model variation
Individual threads/streams
Timeline of operations

---
High level view of operations
Loading graph vars
fprop
Pre-processing
bprop
Device

---
Part 1 Bulk memory transfer & pre-processing (Gpipe)

---
It is also the most expensive call among send/recv

---
Minibatch transfer. This does not take as much time when compared to loading graph variables
For minibatch of dimensions (256,28,28,1), float32, size is 256*28*28*1 *4 = 802816

---
Pre-processing and mem transfer (no gpipe)
Observer that this pre-processing time is similar in both gpipe and w/o gpipe case

---
Part 2: FProp
Fprop computations on gpu 0
Fprop operations on gpu 1
Send

---
First partition’s ops only performed
Output of conv2 is (16,14,14,50), float32. 627200 bytes corresponds to this output

---
Operations on gpu 1
Corresponding recv

---
Last fprop. Done on 16th micro-batch.
The difference in processing a microbatch from one partition to the next becomes increasingly skewed. GPU:0 proceeds with next microbatch without any concern for how much is completed on GPU:1

---
Part 3: BProp
recomputation
Backprop computation done on first split after recv called (not shown in pic)
D2D comm.
Recomp.
Bprop on gpu1

---
This process keeps happening…
recomputation

---
Next minibatch
Happens 16 times (Bprop)

---
Comparisons
2 gpu 2 split gpipe
Estimated time for 5 minibatches
Avg. per minibatch ~124-125 ms

---
2 gpu 1 split, 1 minibatch per gpu, no gpipe (data parallel)
Avg time per minibatch = 592.246/10 = 59.2246 ms

---
2 gpu 1 split, 1 minibatch per gpu, gpipe (data parallel)
Avg time per minibatch ~ 88.3495 ms

---
Compare this value with preprocessing time for non data parallel approach (upcoming slides)
Graph op load time

---
1 gpu 1 split no gpipe (Normal situation)
Avg time per minibatch ~ 74.62 ms

---
The data parallel approach takes approx. 2x time for this stage because gpu:0 processes the minibatches for both gpu:0 and gpu:1 before sending.
No signif. diff with data parallel approach in graph operation load

---
Primary consideration
To evaluate whether Gpipe gives better performance, consider the 1st and last cases from the comparisons. i.e 2 split, 2 gpu, gpipe and 1 split, 1 gpu, no gpipe (normal scenario)

---
Setup times
GPipe
No GPipe
No significant diff in setup times

---
Fprop times
gpipe
No gpipe
Gpipe performs much worse than non-gpipe in this section

---
Fprop times
For most operations, cumulative micro batch time has taken approx. 2-3 times the batch processing case. For FC layer alone, Gpipe takes significantly longer.
Time spent in send/recv/stalls due to them is approx. 21.76 ms - 12.130 ms = 9.63 ms

---
Backprop times

---
Backprop times
gpipe
No gpipe

---
Recomputation time
Recomputation is a part of backprop. Some overlap is there with other backprop operations, but even when this overlap is ignored, the time spent in communication is atleast 45.447ms – 14.816ms – 22.174ms = 8.457 ms.

---
Remarks
Cumulative time spent in comm. does not differ by much between fprop and bprop
This is expected because data sent at boundaries is similar irrespective of fprop/bprop

---
Remarks
The primary bottlenecks seem to be:
The increase in computation times due to splitting rather than batch processing
Communication times between partition boundaries
Recomputation. Might have increasing impact with more layers